## Slide 1
Multi-Preset Video Encoder Bitrate Ladder Prediction
Fatemeh NASIRI
ViSNext’22

## Slide 2: Down-sampling in low bitrate video coding
At low bitrate:
  Number of bits for motion vectors and residual information are comparable.
  Fewer bits for residual  quantization distortion
At high bitrate:
  More bits for residual information
  Up-sampling distortion.
Down-sampling can be beneficial for low bitrate ranges
Low resolution is better
High resolution is better

## Slide 3: Where does video get down-sampled?
HTTP Adaptive Streaming (HAS)
Through different standards and protocols (DASH, HLS etc.)
HTTP server
(hosting video content)
Network
(variable bandwidth)
Client
Internet
Time
Low
Medium
Best
Quality
Time
Bandwidth
Low
Medium
Best
Quality

## Slide 4: Bitrate ladder
16:9 aspect ratio | HEVC/H.265 30 fps | HDR (HEVC) 30 fps | Frame rate
640 x 360 | 145 | 160 | ≤ 30 fps
768 x 432 | 300 | 360 | ≤ 30 fps
960 x 540 | 600 | 730 | ≤ 30 fps
960 x 540 | 900 | 1090 | ≤ 30 fps
960 x 540 | 1600 | 1930 | Same as source
1280 x 720 | 2400 | 2900 | Same as source
1280 x 720 | 3400 | 4080 | Same as source
1920 x 1080 | 4500 | 5400 | Same as source
1920 x 1080 | 5800 | 7000 | Same as source
2560 x 1440 | 8100 | 9700 | Same as source
3840 x 2160 | 11600 | 13900 | Same as source
3840 x 2160 | 16800 | 20000 | Same as source
Static or “One-size-fits-all” bitrate ladder
The main drawback:
  Its recommendation scheme is the same for all video contents, regardless of their spatio-temporal features.
https://developer.apple.com/documentation/http_live_streaming
One static ladder for HEVC

## Slide 5: Bitrate ladder and content dependency
Chart: Bitrate (kbs)
| 2701.9050000000002 | 1963.8975 | 1456.4475 | 1083.375 | 802.54499999999996 | 618.60749999999996 | 468.94499999999999 | 364.90499999999997 | 283.85250000000002 | 225.92250000000001 | 180.51 | 144.95249999999999 | 116.7975 | 94.237499999999997 | 74.174999999999997 | 59.22
540p | 37.101 | 37.0262 | 36.9277 | 36.801 | 36.6252 | 36.4168 | 36.1365 | 35.7722 | 35.3248 | 34.7906 | 34.2035 | 33.4928 | 32.6509 | 31.7706 | 30.8017 | 29.7585
720p | 40.2403 | 40.1077 | 39.939 | 39.7318 | 39.47 | 39.1402 | 38.7265 | 38.2214 | 37.6288 | 36.9403 | 36.1922 | 35.305 | 34.3701 | 33.32 | 32.2074 | 31.0266
1080p | 44.7717 | 44.5195 | 44.2135 | 43.8393 | 43.3953 | 42.8948 | 42.2723 | 41.5465 | 40.7306 | 39.8499 | 38.9033 | 37.9007 | 36.7848 | 35.5846 | 34.3705 | 33.0825
2160p | 47.7562 | 47.1204 | 46.657 | 46.2703 | 45.8334 | 45.357 | 44.8098 | 44.1954 | 43.5089 | 42.7511 | 41.9221 | 41.009 | 40.0143 | 38.9104 | 37.7592 | 36.5732
crossP_1 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
crossP_2 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
crossP_3 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
Chart: Bitrate (kbs)
| 26604.052500000002 | 22247.88 | 17918.849999999999 | 14316.9825 | 11058.6 | 8626.6949999999997 | 6027.1875 | 4284.6374999999998 | 2744.07 | 1736.2874999999999 | 1061.8050000000001 | 630.13499999999999 | 365.07 | 206.91749999999999 | 118.3275 | 70.237499999999997
540p | 33.8797 | 33.7655 | 33.5602 | 33.2944 | 32.8652 | 32.3893 | 31.5603 | 30.791 | 29.87 | 29.0894 | 28.4453 | 27.9376 | 27.5196 | 27.1749 | 26.8889 | 26.6463
720p | 35.9535 | 35.7895 | 35.502 | 35.1398 | 34.5767 | 33.9806 | 32.9909 | 32.1109 | 31.0769 | 30.1281 | 29.2617 | 28.5835 | 28.0362 | 27.5905 | 27.2292 | 26.9213
1080p | 39.5577 | 39.2434 | 38.743 | 38.1576 | 37.3229 | 36.5038 | 35.2486 | 34.1973 | 33.0026 | 31.8913 | 30.8151 | 29.8672 | 29.0764 | 28.4177 | 27.8781 | 27.4374
2160p | 45.0954 | 44.2099 | 43.0823 | 42.0847 | 40.9706 | 39.9873 | 38.5986 | 37.4739 | 36.2259 | 35.0896 | 33.9545 | 32.8557 | 31.7813 | 30.7593 | 29.8435 | 29.0316
crossP_1 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
crossP_2 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
crossP_3 | 25 | 27 | 29 | 31 | 33 | 35 | 37 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 53 | 55
Complex content
Simple content

## Slide 6: Content-adaptive bitrate ladder
  They obtain R-D points by running several trial encodings
  Construct the convex hull
  PSNR and VMAF
Netflix (Per-title encoding)
Bitmovin (Per-title encoding )
Efficient Bitrate Ladder Construction (Katsenou, A , et al.)
  Complexity analysis, Feature extraction
  ML-based method to predict the convex hull and construct the adjusted bitrate ladder.
  ML-based method
  Predicts the cross-over points in R-D curves.
  Fixed QP
  PSNR and VMAF
Katsenou, A. V., Sole, J., & Bull, D. R. (2021). Efficient bitrate ladder construction for content-optimized adaptive video streaming. IEEE Open Journal of Signal Processing, 2, 496-511.

## Slide 7: Bitrate Ladder Construction Multi-preset ML-based Bitrate Ladder Construction

## Slide 8: Content-specified bitrate ladder
: Input video
: target bitrate
: resolution
: Encoder
: quality index
Scaled PSNR
Log(Bitrate (kbps))
Full rate-quality points

## Slide 9: Content-specified bitrate ladder
: Best quality
: Encoder
Scaled PSNR
Log(Bitrate (kbps))
: Convex-hull
Scaled PSNR
Log(Bitrate (kbps))
Full rate-quality points
Convex-hull

## Slide 10: Content-specified bitrate ladder
Resolution Index
Log(Bitrate (kbps))
Scaled PSNR
Log(Bitrate (kbps))
Cross-over bitrate
Bitrate ladder
index of the optimal resolution
Cross-over bitrates
Bitrate ladder

## Slide 11: Fast-pass method
Multi-preset encoder
5 presets in VVenC encoder:
  “Faster”
  “Fast”
  “Medium”
  “Slow”
  “Slower”
Estimate a slower preset’s bitrate ladder from a faster preset’s bitrate ladder
The relative position of cross-point bitrates of the “slow” preset of VVenC, with respect to its “faster” preset.

## Slide 12: Fast-pass method
A slow preset bitrate ladder
A fast preset bitrate ladder
video

## Slide 13: Fast-pass method: training
Signal feature extractor
Train model M
Model M
slow
fast
(Ground truth)
Concatenate
fast
slow
slow
fast
Test
slow
Train
slow

## Slide 14: Bitrate Ladder Construction Experimental Results

## Slide 15: Results/ Dataset
Different resources: BVI SR, Derf collection, MCML, UHD videos, 4:2:0, 8 bits
Segment duration: 1 second
Features:
  Gray level concurrence matrix
  Temporal coherency
Spatial Index (SI)
Temporal Index (TI)

## Slide 16: Results/ Reference convex hull construction
Four resolutions: 2160p, 1080p, 720p and 540p.
Encoded with VVenC, “faster” preset
Convex-hull is constructed for all segments in the training dataset.
To avoid overfitting, we used the 10-fold random cross validation.
Regressor: Gradient process.
Scaled PSNR
Log(Bitrate (kb/s))

## Slide 17: Results/ Fast-pass
Preset bitrate ladder predicted from “faster” bitrate ladder | BD-BR vs GT | BD-BR vs Static | Acceleration of the proposed method compared to GT
“Fast” | 0.79% | -9.44% | 25%
“Medium” | 0.67% | -8.60% | 75%
“Slow” | 0.88% | -8.32% | 91%
Loss, since we are avoiding full bitrate-quality points calculation in GT
Gain, since we are adapting the bitrate ladder to content

## Slide 18: Conclusion

## Slide 19: Conclusion
Down-sampling is beneficial in adaptive video streaming
The static “one-size-fits-all” bitrate ladder has obvious drawbacks
We proposed a machine learning method for bitrate ladder prediction of a slow preset from a fast preset of the same encoder.
Significant compression gain when ladder is predicted with our method compared to static bitrate ladder